## Slide 1: When should Spacecraft Launches happen?
By Junyan Peng

## Slide 2: Motivation
Space travel has been a human interest both for resources and for discovery
Calculations needed for determining conditions for spacecraft launches are complex and inefficient to compute by hand
Modeling algorithms for spacecraft are usually time-step processes that are convenient for computer computation

## Slide 3: Proposal
By programming time-step algorithms and applying it to spacecraft and planets over a time period, the closest to present date and angle for a launch that takes you to a specified planet in the minimum amount of time can be accurately and efficiently calculated.

## Slide 4: Orbit Calculation
Newton-Raphson Method that uses Keplerian elements as parameters to calculate the angular change of an object in orbit relative to the object its orbiting
Used starting position from NASA’s database to find starting angular position of a planet in its orbit relative to the sun

## Slide 7: Spacecraft Calculation
Initial speed of spacecraft on verge of leaving a planet found from Apollo moon mission data along with gravitational field at that point
This strength of that g field will be used to determine if a rocket has reached a planet
Fourth-order runge-kutta method of numeric integration allows for greater accuracy than just using the universal law of gravitation

## Slide 10: Future Tasks
Defining what it means to be within the range of a planet for small planets
Finding a better way to determine the mean anomaly for the current position of a planet as current method only works for Mercury
Implementing time variable and UI
Eliminating unnecessary angles and adding parallel for efficiency

## Slide 11: References
https://photos.com/featured/earth-view-from-outer-space-background-cybrain.html?product=acrylic-print
https://www.researchgate.net/figure/Geometric-interpretation-of-the-fourth-order-Runge-Kutta-method_fig13_299354655
https://www.planetary.org/multimedia/space-images/charts/diagram_orbit_ephemeris_definitions.html